In this project, you are asked to design a 32-bit ALU. It will be part of a single-cycle processor and will handle a small portion of the MIPS instruction set. This portion of the MIPS instruction set is:
arithmetic: add, sub
logical: and, or, sll
conditional: slt, sltu
Details about these instructions can be found in the front and back of your text. Please use only the components provided in the Projects folder under the Files tab (eecs361lib.tar.gz).
Information about the design can be found in the class notes or on Appendix B of the textbook.

NOTE: You must have the following input/output signals in your ALU:
Input: Operand A (32 bits), Operand B (32 bits), Control signals (at least 3 bits)
Output: Carryout, Overflow, Zero, Result (32 bits)
THINGS TO TURN IN:
1) VHDL code for each individual bit.
2) VHDL code of all 32 bits (with appropriate connections of course).
3) A trace/simulation of an individual bit.
4) A trace/simulation of 32 bits working in harmony.
Note that this is an individual assignment; each student should turn in his/her original work.
The deadline for the project is end of day, Thursday, October 30th. Please turn in your homework using Canvas.